## Slide 1
GROUP 24 · LITERATURE REVIEW SUPPLEMENT
Noise Reduction in
Rheological Signal Processing
Preserving gel transitions while eliminating instrument noise
5 Key Papers
6 Techniques
Haemograph Project
Data Science
Wavelet Analysis
Wavelet-Based Time–Frequency Analysis of Evolving Fluids in a Microfluidic Rheometer

## Slide 2
THE CORE CHALLENGE — NOISE VS USEFUL SIGNAL
The central question raised by Dr Ragil: is useful information being rejected while removing noise?
WHAT IS NOISE IN RHEOMETER DATA?
Instrument vibration and mechanical artefacts from the rheometer motor
Thermal fluctuations causing baseline drift in storage/loss moduli
Electrical noise in sensor output (ADC quantisation noise)
Environmental interference: air currents, building vibration
Additive Gaussian white noise distributed across all frequencies
High-frequency components uncorrelated with material behaviour
WHAT MUST NOT BE REMOVED?
Rapid transient jumps at the gel point — mark onset of structural transition
Harmonic content at frequencies above the fundamental — encodes nonlinear viscoelastic behaviour
Small amplitude modulations tracking evolving moduli — may be real signal
Dominant frequency shifts over time — captures gelation kinetics
Structural transition markers — scale drift and harmonic energy redistribution
Key metric: Evaluation must measure feature preservation, not just SNR improvement

## Slide 3
THE DENOISING DILEMMA
Why noise reduction in evolving rheological signals is fundamentally different
THE PROBLEM
In a stationary signal, noise reduction is straightforward — apply a low-pass filter or average.
But gelation signals are non-stationary by design:
The gel point crossover IS a rapid change in G′. A filter that smooths noise also smooths the transition you are trying to detect.
OVER-SMOOTH
Window too wide — gel point blurred, crossover time wrong
UNDER-SMOOTH
Window too narrow — noise spikes misidentified as transitions
Key insight: The window size must be chosen relative to the expected gelation timescale — which varies between experiments and concentrations. This is why adaptive methods (wavelets, EMD, VMD) outperform fixed-window filters for your data.
Recommended pipeline: Ensemble avg → Savitzky-Golay preprocessing → Wavelet CWT analysis → EMD/VMD decomposition

## Slide 4
PAPER 1 — OWCh: THE NOISE-SIGNAL FOUNDATION
Geri, Keshavarz, Divoux, Clasen, Curtis, McKinley (2018). Physical Review X, 8, 041042.
DOI: 10.1103/PhysRevX.8.041042 | Free PDF: arxiv.org/abs/1804.03061
WHAT IT PROVED
OWCh reduces measurement time by up to 100× vs conventional frequency sweeps
Cosine-tapered window simultaneously minimises spectral leakage AND maximises SNR
Optimal tapering ≈ 10% of total signal length
Accuracy limited only by the instrument's noise floor — not the method
Demonstrated on fast gelation of acid-induced protein gel — direct predecessor of Haemograph application
THE NOISE INSIGHT
As the tapering parameter increases:
↓ Spectral leakage decreases
↓ Signal power at edges decreases
↓ SNR of output deteriorates
→ Optimal window balances both effects — this is where the name 'optimally windowed' comes from.
Dataset 1 connection: Mills et al. (2025) used OWCh on an ARES-G2. This paper invented the method. The noise floor analysis directly explains the TransientMotorTorque column.

## Slide 5
PAPERS 2 & 3 — WAVELET DENOISING: THEORY & PRACTICE
PAPER 2
Donoho & Johnstone (1994) Biometrika, 81(3), 425–455 DOI: 10.1093/biomet/81.3.425 | PDF: imjohnstone.su.domains/WEBLIST/1994/isaws.pdf
PAPER 3
Donoho (1995) IEEE Trans. Inf. Theory, 41(3), 613–627 DOI: 10.1109/18.382009 | PDF: web.stanford.edu/dept/statistics/cgi-bin/donoho/wp-content/uploads/2018/08/denoiserelease3.pdf
1994 — THE ORACLE INEQUALITY
Proved wavelet thresholding is near-optimal. Even without knowing which coefficients carry signal vs noise, a simple threshold achieves near-oracle performance.
Universal threshold: λ = σ √(2 log N)
where σ = noise std, N = signal length
In PyWavelets:
pywt.threshold(coeffs, value=σ·√(2·log(N)), mode='soft')
HARD THRESHOLDING
Zero coefficients below λ, keep rest unchanged.
✓ Preserves sharp boundaries and transient jumps
✗ Discontinuous at threshold — causes Gibbs oscillations near signal edges
⚠ For gel crossover: may introduce artificial jumps that mimic transition events
SOFT THRESHOLDING — PREFERRED
Shrink all coefficients toward zero by λ.
✓ Smooth reconstruction, no discontinuities
✓ Preserves smoothness class of true signal
✗ Over-smooths, underestimates amplitude
⚠ Preferred for G′/G″ — gel point crossover is a smooth inflection, not a sharp step

## Slide 6
PAPERS 4 & 5 — EMD AND SAVITZKY-GOLAY
Huang, Shen, Long et al. (1998) Proc. Royal Society A, 454(1971), 903–995 DOI: 10.1098/rspa.1998.0193 | Free PDF: hal.science/hal-04014501v1/file/huang1998.pdf
1
Find extrema
Identify all local maxima and minima of the signal
2
Fit envelopes
Cubic spline through maxima (upper) and minima (lower)
3
Extract IMF
Subtract mean envelope — repeat sifting until convergence
What the IMFs represent for gelation data:
IMF 1–2 (fast noise)
Instrument electrical noise, vibration — DISCARD
IMF 3–5 (gelation dynamics)
Actual G′ rise — PRESERVE
Residual (trend)
Slow monotonic increase — core gelation signal
Savitzky & Golay (1964) Analytical Chemistry, 36(8), 1627–1639. 20,000+ citations DOI: 10.1021/ac60214a047 | Free PDF: agora.cs.wcu.edu/~huffman/figures/sgpaper1964.pdf
The Key Idea
Fit a polynomial to each sliding window by least squares. Use the polynomial value at the window centre as the smoothed estimate. This preserves peaks, troughs and shape — unlike a moving average which flattens them.
Moving Avg
Savitzky-Golay
Peak shape
Flattened
Preserved
Phase shift
Yes
None
Gel point time
Shifted
Accurate
OWCh Dataset 1: Window < one chirp period (~14 s). Gelation Dataset 2: Window < gel point transition time (~3–5 measurement intervals at 13.4 s/pt).

## Slide 7
VMD AND HYBRID APPROACH — MOST PROMISING FOR THIS PROJECT
VMD — VARIATIONAL MODE DECOMPOSITION
Dragomiretskiy & Zosso (2014) IEEE Trans. Signal Processing, 62(3), 531–544 DOI: 10.1109/TSP.2013.2288675
VMD addresses EMD's mode mixing problem by solving a constrained variational problem — it simultaneously estimates K band-limited modes and their centre frequencies.
It is mathematically grounded, non-recursive, and includes an internal Wiener filter for noise robustness.
Why VMD suits this project:
• Separates fundamental, harmonics and drift into distinct modes
• Robust to noise without mode mixing — critical for harmonic preservation
• Key parameters to tune: number of modes K and penalty factor α
RECOMMENDED HYBRID PIPELINE
01
VMD Decomposition
Decompose the chirp rheometer signal into K band-limited modes (fundamental + harmonics + drift). Tune K and α to the data.
02
Wavelet Thresholding per VMD Mode
Apply adaptive layer-dependent threshold within each mode. High-frequency layers → soft thresholding. Low-frequency layers → hard thresholding.
03
Feature Extraction
Reconstruct denoised signal. Extract dominant frequency evolution, amplitude modulation, harmonic content, and structural transition markers for M3 / M4.
Evidence: Kaur & Bhatt (2015) — VMD-DWT hybrid outperforms EMD-DWT across all SNR/MSE metrics on ECG | Shi et al. (2025) — EEMD+entropy+IWTD best preserves transient features

## Slide 8
THRESHOLD SELECTION — THE CRITICAL PARAMETER
Too large a threshold removes useful signal. Too small and noise remains. Selection method determines outcome.
Universal Threshold
(VisuShrink)
OVER-REMOVES
Formula: λ = σ√(2 log n)
Threshold derived from noise level σ and signal length n. Simple and robust but often set too large — removes useful coefficients in evolving signals.
Donoho & Johnstone (1994) doi.org/10.1093/biomet/81.3.425
SURE Threshold
(Stein's Unbiased Risk)
UNSTABLE
Formula: Minimises MSE estimate
Adapts to signal energy. More accurate than universal for most signals but has high variance when signal energy is below noise energy — unstable for weak transient events.
Minimax Threshold
BALANCED
Formula: Near-optimal worst-case
Provides near-minimax optimal risk — sits between Universal and SURE. Good general performance. More conservative than Universal, preserving more signal structure.
Interscale Correlation
Threshold
★ RECOMMENDED
Formula: Propagation across scales
Uses propagation of wavelet coefficients across decomposition levels. Noise coefficients do not correlate across scales; signal does. Most appropriate for transient feature preservation.
He et al. (2015) doi.org/10.1155/2015/280251

## Slide 9
COMPARATIVE SUMMARY — ALL METHODS
Evaluated against the criteria that matter for evolving fluid / coagulation signal analysis
Method
Non-stationary
Transient Preservation
Harmonic Content
Complexity
Recommended
FFT Filtering
✗ No
✗ Poor
✗ Lost
Low
✗ No
Wavelet Hard
Partial
✓ Good
Partial
Medium
Baseline only
Wavelet Soft
Partial
✗ Over-smooths
✗ Weakened
Medium
✗ No
Adaptive WT (ALDTF)
✓ Yes
✓ Good
✓ Preserved
Med-High
✓ Phase 1 test
EMD / EEMD
✓ Yes
Moderate
Moderate
Medium
Comparison
VMD
✓ Yes
✓ Good
✓ Preserved
Med-High
✓✓ Primary
VMD + Wavelet Hybrid
✓ Yes
✓✓ Best
✓✓ Best
High
✓✓ Recommended

## Slide 10
KEY PAPERS — FULL REFERENCES & LINKS
OWCh
Geri et al. (2018). Time-Resolved Mechanical Spectroscopy via Optimally Windowed Chirps. Physical Review X, 8, 041042.
DOI: 10.1103/PhysRevX.8.041042
Free: arxiv.org/abs/1804.03061 | MIT: dspace.mit.edu/handle/1721.1/119797
Wavelet Theory
Donoho & Johnstone (1994). Ideal Spatial Adaptation by Wavelet Shrinkage. Biometrika, 81(3), 425–455.
DOI: 10.1093/biomet/81.3.425
Free: imjohnstone.su.domains/WEBLIST/1994/isaws.pdf
Soft Threshold
Donoho (1995). De-Noising by Soft-Thresholding. IEEE Trans. Information Theory, 41(3), 613–627.
DOI: 10.1109/18.382009
Free: web.stanford.edu/dept/statistics/cgi-bin/donoho/wp-content/uploads/2018/08/denoiserelease3.pdf
EMD
Huang et al. (1998). Empirical Mode Decomposition and the Hilbert Spectrum. Proc. Royal Society A, 454(1971), 903–995.
DOI: 10.1098/rspa.1998.0193
Free: hal.science/hal-04014501v1/file/huang1998.pdf
S-G Filter
Savitzky & Golay (1964). Smoothing and Differentiation by Simplified Least Squares. Analytical Chemistry, 36(8), 1627–1639.
DOI: 10.1021/ac60214a047
Free: agora.cs.wcu.edu/~huffman/figures/sgpaper1964.pdf
VMD
Dragomiretskiy & Zosso (2014). Variational Mode Decomposition. IEEE Trans. Signal Processing, 62(3), 531–544.
DOI: 10.1109/TSP.2013.2288675
Available via IEEE Xplore
Interscale Threshold
He et al. (2015). A new wavelet threshold considering interscale correlation. Mathematical Problems in Engineering, 2015, 280251.
DOI: 10.1155/2015/280251
Open access: Wiley Online Library
ALDTF 2025
Adaptive Layer-Dependent Threshold Function (ALDTF) for ECG/cardiopulmonary signals. PMC 2025.
Available via: PubMed Central (PMC)
VMD Hybrid
Kaur & Bhatt (2015). Comparative study: ECG denoising by wavelet thresholding in EMD and VMD domains. IET Signal Processing / PMC.
Available via PubMed Central
EEMD Transient 2025
Shi et al. (2025). EEMD-SE-IWTD combined noise reduction for high-speed transient features. Sensors, 25, 5940.
DOI: 10.3390/s25195940
Open access: MDPI Sensors

## Slide 11
APPLICATION TO THIS PROJECT — M3, M4 & EVALUATION FRAMEWORK
M3 — NOISE CHARACTERISATION (Wks 6–8)
Quantify SNR, noise type, and spectral distribution across ROTEM/TEG 6S and gel datasets
Identify which signal features degrade first under noise (harmonics, transients, amplitude)
Test whether Gaussian, impulse, or drift noise dominates the rheometer output
Establish SNR baseline before any denoising — becomes the pass/fail reference
M4 — BASELINE METHOD (Wks 8–11)
Implement FFT, STFT and CWT pipelines with consistent preprocessing and noise handling
Test wavelet hard vs soft vs adaptive threshold on gel signal datasets
Apply VMD decomposition and compare denoised output against FFT-filtered baseline
Evaluate feature preservation: dominant frequency, harmonic content, gel-point transient
PASS / FAIL CRITERIA
SNR improvement ≥ target threshold (defined from M3 baseline)
Amplitude of dominant frequency preserved within acceptable error bound
Gel-point transient not smoothed away — detectable in denoised signal
Real-time processing feasibility: denoising latency within FPGA constraint
Recommended reading order: (1) Donoho & Johnstone 1994 → (2) Geri et al. 2018 → (3) Huang et al. 1998 → (4) Savitzky & Golay 1964 → (5) Donoho 1995 → (6) Dragomiretskiy & Zosso 2014